A + B Simulator Instructions

Parts List:

1.Main Frame

2.Front support

3.Monitor mount

4.Rear base

5.Seat supports

6.Computer mount

7.Shifter mount

8.Steering wheel mount

9.Seat

10.3/16” T-Handle Wrench

11.6mmx50mm screws/washers (4)-wheel/shifter

12.6mmx20mm screws/washers(6)-pedals

13.4mmx20mm screws/washers(12)-monitors

14.Slot cap (36”)

Step 1:

Attach the seat to the seat supports using (4) 5/16”x1/2” button head bolts and 5/16” nuts.  Move the seat slider to gain access to the mounting holes.

Step 2:

Slide the seat onto the main frame, align the seat supports up with the access holes and tighten the (4) bolts.

Step 3:

Slide the rear base on to the main frame and tighten the (4) bolts through the access holes.  Tighten the (2) end plate bolts.

Step 4:

Slide the gear shifter mount on the main frame and tighten the (2) bolts.

Step 5:

Slide the computer mount on the main frame and tighten the (1) bolt using the access hole from the bottom side.

Step 6:

Slide the front support on the main frame and tighten the (4) bolts through the access holes from the bottom side.

Step 7:

Attach the monitor mount to the top of the front support.  Line up the bolts located inside the mount and tighten the (2) bolts through the access holes.

Step 8:

Slide the steering wheel mount onto the front support and tighten the (4) bolts.  Tighten the (4) end plate bolts.

Step 9:

Attach the wheel with the (2) 6mmx50mm screws/washers.  Insert bolts through the mount and tighten and secure the wheel clamp.

Step 10:

Attach the pedal s with the (6) 6mmx20mm screws/washers.  Insert through the base and tighten.

Step 11:

Attach the shifter with the (2) 6mmx50mm screws/washers.  Insert through the mount and tighten and secure with the clamp.

Step 12:

Attach the monitors to the monitor brackets with the (12) 4mmx20mm screws/washers.  Tighten the top and bottom bolts of the center monitor bracket.  The two side monitors can be adjusted by sliding the bracket on the mount.  Adjust the angle and position and tighten the top and bottom bolts of the brackets and pivot points.

Step 13:

Adjust the support rails on the computer mount to match the width of the computer and tighten the bolts.  Set the computer on the mount.

Step 14:

Route the wires for all of the components inside the slots where possible.  Cut the slot cap material to the correct size and snap in the slot to hold the wires in place.